## Slide 1
Vaccine Storage and Handling
Presentation to:
Presented by:
Date:

## Slide 2: Disclosure Statements
Neither the planners of this session nor I have any financial relationship with pharmaceutical companies, biomedical device manufacturers, or corporations whose products and services are related to the vaccines we discuss.
There is no commercial support being received for this event.
The mention of specific brands of vaccines in this presentation is for the purpose of providing education and does not constitute endorsement.
The GA Immunization Office utilizes ACIP recommendations as the basis for this presentation and for our guidelines, policies, and recommendations.
For certain vaccines this may represent a slight departure from or off-label use of the vaccine package insert guidelines.
Notes: [Presenter is required to read this information to the audience before the program begins.]
Neither the planners of this session nor I have any financial relationship with pharmaceutical companies, biomedical device manufacturers, or corporations whose products and services are related to the vaccines we discuss.
There is no commercial support being received for this event.
The mention of specific brands of vaccines in this presentation is for the purpose of providing education and does not constitute endorsement.
The GA Immunization Office utilizes ACIP recommendations as the basis for this presentation and for our guidelines, policies, and recommendations.
For certain vaccines this may represent a slight departure from or off-label use of the vaccine package insert guidelines.

## Slide 3: Disclosure Statement
To obtain nursing contact hours for this session, you must be present for the entire session and complete an evaluation.
Continuing education will be provided through the Georgia Department of Public Health
Georgia Department of Public Health is an approved provider of continuing nursing education by the Alabama State Nurses Association, an accredited approver by the American Nurses Credentialing Center’s Commission of Accreditation

## Slide 4: Objectives
Define and explain vaccine cold chain management
Review required storage equipment units for vaccine storage and handling
Identify thermometers recommended to monitor storage unit temperatures
Discuss the components of routine and emergency plans for vaccine storage and handling
Notes: Presenter to review objectives and goals for presentation based on content outline

## Slide 5: Introduction
Proper vaccine storage and handling practices play a very important part in preventing and eradicating vaccine-preventable diseases. Failure to adhere to required protocols for storage and handling can reduce vaccine potency, resulting in inadequate immune response in the recipients and poor protection against disease. Vaccine quality is a shared responsibility of everyone, from the time vaccine is manufactured until it is administered.

## Slide 6
Vaccine Cold Chain
Vaccine Cold Chain relies on 3 main elements:
-A well-trained staff
-Reliable storage and temperature monitoring equipment
-Accurate vaccine inventory management
Notes: Vaccines must be stored appropriately from the time they are manufactured until the time they are administered to a patient. Excessive heat or cold can reduce vaccine potency, increasing the risk that recipients will not be protected against vaccine-preventable diseases. A temperature-controlled environment used to maintain and distribute vaccines in optimal condition is called the vaccine cold chain. The vaccine cold chain relies on three main elements:
A well-trained staff;
Reliable storage and temperature monitoring equipment, and;
Accurate vaccine inventory management.
All three elements must stay consistent to ensure vaccines are transported and stored appropriately.
The vaccine cold chain begins with the cold storage unit at the vaccine manufacturing plant, extends through the transport of vaccine to the distributor, then delivery to the provider, and ends with the administration of the vaccine to the patient. Appropriate storage temperatures must be maintained at every link in the chain.
Vaccine should always be transported in a refrigerated or frozen state. Refer to manufacturer protocols for each vaccine. Transport should include use of an insulated container or refrigerated truck. Appropriate temperatures are: Refrigerator between 35°F and 46°F [2°C and 8°C] Freezer between -58°F and +5°F [-50°C and -15°C]

## Slide 7: Cold Chain Management
  Vaccine Potency
Excessive heat or cold exposure can damage vaccines
Each time vaccines are exposed to excessive heat or cold, reduced potency increases
Inappropriate storage conditions can be costly. Vaccines are very expensive
Notes: Eventually, if the vaccine cold chain is not properly maintained, all potency will be lost, and the vaccines become useless. While exposure to both warm and cold temperatures can affect the potency of refrigerated vaccines, a single exposure to freezing temperatures will destroy some refrigerated vaccines. HepB and DTaP/DT/Tdap/Td vaccines are especially sensitive to freezing temperatures. That is why it is important to regularly monitor the temperature of your vaccines and take immediate corrective action when a storage unit temperature reading is outside the recommended range (temperature excursion).
Vaccine Appearance after Exposure to Inappropriate Storage Conditions
Some vaccines may show physical evidence that potency has been reduced when exposed to inappropriate storage conditions. This may appear as clumping in the solution that does not go away when the vial is shaken.
Other vaccines may look perfectly normal when exposed to inappropriate storage conditions.
For example, inactivated vaccines exposed to freezing temperatures (i.e., 32°F [0°C] or colder) may not appear frozen and give no indication of reduced or lost potency. Therefore, visual inspection of vaccines must be considered unreliable when assuring vaccine was stored under appropriate conditions.
In the General Recommendations on Immunization, the Advisory Committee on Immunization Practices (ACIP) recommends “vaccine exposed to inappropriate temperatures that is inadvertently administered generally should be repeated.”4 Providers should contact their state/local health department immunization program, vaccine manufacturer(s), or both for guidance. Recalling patients to repeat vaccine doses should be considered. Vaccine recalls due to inappropriate storage can mean extra doses for patients, increased costs for providers, and damage to public confidence in vaccines. They can also be a liability for a provider’s practice. Patients who refuse revaccination can remain unprotected from serious, vaccine-preventable diseases.
The costs associated with loss and replacement vaccines, and resources necessary to conduct a recall of patients, can be significant

## Slide 8: Cold Chain Management
Assign responsibility of handling vaccines: primary and back-up staff
Check vaccine shipments
Store vaccines in appropriate type of refrigerator
Store vaccines in appropriate place in the refrigerator
Check temperatures and document temperatures
Take action if temperatures are out of range
Check expiration dates & rotate stock
Have routine and emergency vaccine handling plan
Take other preventive measures
Notes: Now lets look at some tips for protecting our vaccines. The handout “Temperature TIPS for Vaccine Storage” summarizes the general principles discussed in this guidance.

## Slide 9: Vaccine Coordinator
Assign primary responsibilities to one person
Designate a back-up person
Train all office staff working with vaccines
Notes: #1: Assign Responsibility for Handling Vaccine:
Each facility should designate one staff member to be the primary vaccine coordinator. This person will be responsible for ensuring that all vaccines are stored and handled correctly. Vaccine storage and handling responsibilities include but are not limited to the following tasks:
Each facility should assign one person primary responsibility for ensuring that vaccines are carefully handled in a safe, documented manner.
Since no one works every single day, a back-up person should also be designated.
All office staff working with vaccines should be familiar with storage and handling guidelines. Even the receptionist or temporary staff should know what to do with a shipment of Varicella or MMRV if it’s delivered and no one else is present.

## Slide 10: Coordinator Responsibility
Ordering vaccines/Rotating stock
Overseeing proper receipt and storage of vaccine shipments
Organizing vaccines within the storage unit(s)
Reading and manually documenting storage unit temperatures twice per day/responding to temperature excursions
Ensuring that designated staff is adequately trained
Reading and documenting storage unit minimum/maximum temperatures
Downloading and reviewing stored temperature monitoring data at least once per week
Inspecting storage unit(s) daily
Overseeing vaccine transport during emergencies
Maintaining storage equipment and records, including VFC program documentation in participating facilities

## Slide 11: Alternate Vaccine Coordinator
Each office should also designate at least one alternate vaccine coordinator who can assume these same responsibilities in the absence of the primary vaccine coordinator.
The primary and alternate vaccine coordinators should be fully trained regarding routine and emergency policies and procedures related to vaccine shipments, storage, handling, transport, and inventory management.

## Slide 12: Other Staff/Training
All staff members who handle or administer vaccines should be familiar with storage and handling policies and procedures
Staff who handle and administer vaccines should receive comprehensive training regarding storage and handling policies and procedures. This training should be integrated into new staff orientation
Notes: Other Staff
All staff members who handle or administer vaccines should be familiar with the storage and handling policies and procedures at their facility. This includes not only those who administer vaccines, but also anyone who delivers or accepts shipments or who may have access to the unit(s) where vaccines are stored.
Training
Staff who handle and administer vaccines should receive comprehensive training regarding storage and handling policies and procedures. This training should be integrated into new staff orientation. In addition, training should occur whenever recommendations are updated and when new vaccines are added to the facility’s inventory to maintain staff competency. Accountability checks should be put in place to ensure policies and procedures are followed.

## Slide 13: Equipment
Notes: While CDC does not recommend specific brands of vaccine storage units, CDC does provide guidance on types of storage units that offer greater assurance of proper temperatures for vaccine storage based on equipment testing by the National Institute of Standards and Technology (NIST).
Purchasing new vaccine storage equipment may require planning and existing equipment may need to be used for a certain amount of time until new equipment can be purchased. In this situation, CDC recommends using a combination refrigerator/freezer unit for refrigerated vaccine only. A separate stand-alone freezer should be used to store frozen vaccines.

## Slide 14: Storage Requirements
Be large enough to hold the year's largest inventory
Have enough room to store water bottles and coolant packs
Have a calibrated thermometer inside each storage unit
Reliably maintain the appropriate vaccine storage temperatures year-round
Dedicated to the storage of vaccines. Food and beverages should NOT be stored in a vaccine storage unit
Notes: The refrigerator and freezer units must:
Have enough room to store the year’s largest inventory without crowding;
Have enough room to store water bottles (in the refrigerator) and frozen coolant packs (in the freezer) to stabilize the temperatures and minimize temperature excursions that can impact vaccine potency. The addition of water bottles in the refrigerator (not coolant packs) reduces the risk of freezing due to the tremendous latent heat released from water prior to freezing;
Have a calibrated thermometer inside each storage unit; Reliably maintain the appropriate vaccine storage temperatures year-round;
Be dedicated to the storage of vaccines. Food and beverages should NOT be stored in a vaccine storage unit because this practice results in frequent opening of the door and destabilization of the temperature.

## Slide 15: Storage Requirements
Refrigerator
Store vaccines between
2°C and 8°C
(36°F and 46°F)
Freezer
Store vaccines between
-50°C and -15°C
(-58°F and +5°F)
Stand-alone freezer
Stand-alone refrigerator
Notes: CDC recommends stand-alone units, meaning self-contained units that only refrigerate or freeze, and are suitable for vaccine storage. These units can vary in size, from compact, under-the-counter style to large, stand-alone, pharmaceutical grade units.
Proper Vaccine Storage Temperatures
Refrigerated vaccines should be stored at temperatures between 2° C and 8° C (36° F and 46°
F). The thermostat should be set at midrange to achieve a temperature of about 5° C (40° F),
which will decrease the likelihood of temperature excursions.
Vaccines stored in the freezer should maintain temperatures between -50° C and -15° C (-58°
F and +5° F). The thermostat should be at the factory-set or midpoint temperature setting to
assure appropriate frozen storage temperatures. The new recommended Fahrenheit temperature range is between 36° F and 46° F (previously between 35° F and 46° F). The Celsius temperature range (between 2° C and 8° C) remains unchanged, as stated in all manufacturer package inserts for routinely recommended vaccines.
Stabilizing Temperatures in New and Repaired Units
It may take 2 to 7 days to stabilize the temperature in a newly installed or repaired refrigerator or
2 to 3 days for a freezer. Before using a unit to store vaccines, check and record temperatures a
minimum of 2 times each workday for 2 to 7 days.

## Slide 16
Refrigerated vaccines ONLY
FREEZER
Household combination refrigerator/freezer
Do not store any vaccine in a dormitory-style or bar-style combined refrigerator/freezer unit under any circumstances.
Notes: If you must use a household-grade combination refrigerator/freezer unit, only use the refrigerator compartment for storing vaccines. These units have cold spots and temperature fluctuations, and air circulating from the freezer could expose refrigerated vaccines to freezing temperatures. Use a separate stand-alone freezer to store frozen vaccines.
Do not store any vaccine in a dormitory-style or bar-style combined refrigerator/freezer unit under any circumstances. These units have a single exterior door and an evaporator plate/cooling coil, usually located in an icemaker/freezer compartment. These units have been shown to pose a significant risk of freezing vaccines, even when used for temporary storage. (Note: Not all small storage units are dormitory- or bar-style units. Compact purpose-built units for biologics can be used to store vaccines.)

## Slide 17: Refrigerator-only Unit

## Slide 18: Stand-alone Freezer

## Slide 19: Refrigerator Set-Up
Unit location
Guidelines – 4 to 6 inches of clearance around outside of unit (Check manufacturer manual to verify minimum spacing)
Well-ventilated room for maintaining ambient conditions within manufacturer specifications
Startup
Remove any vegetable/ dairy bins (not suitable for vaccine storage)
Place filled water bottles in areas where vaccine storage is prohibited
Notes: Water bottles and frozen coolant packs will help maintain stable temperatures with frequent opening and closing of unit doors, in the event of a power failure, and serve as a physical barrier to placing vaccines in an area where there is greater risk for temperature excursions. Place water bottles on top shelf, floor, and in door racks of refrigerator. The Joint Commission on Accreditation of Healthcare Organizations (Joint Commission) does not recommend storage of food or beverages in a medication storage unit, so label water bottles “Do NOT Drink.”
Place frozen coolant packs along walls, back, and bottom of freezer, and inside door racks.
Place items in unit doors carefully so they cannot dislodge, and prevent doors from closing or
weighing them down so much that seals are not tight.

## Slide 20: Freezer Set-Up
Notes: You can help stabilize the temperature in the freezer by keeping frozen coolant packs inside. Store the frozen coolant packs along the walls, back, and bottom of the freezer and inside the racks of the freezer door.
Frozen coolant packs in the freezer door and water containers in the refrigerator door should be placed securely so they cannot dislodge and prevent unit doors from closing. In addition, caution must be taken to avoid weighing down a door so much that the seal is compromised when the door is closed. Not only will water bottles and frozen coolant packs help maintain even temperatures in the storage unit with frequent opening and closing of the doors, they will also help to keep the temperatures stable in the event of a power failure.

## Slide 21: Storage Unit Maintenance
Read and document the internal temperature
Check that each unit door is closed
Monthly Maintenance
Clean the coils and motor
Clean the refrigerator and freezer unit
Check the door seal
Periodic Maintenance
Clean the drain pan
Daily Maintenance
Notes: General Principles
The most important action to take if vaccine storage units are not working properly is to protect the vaccine supply.
The most important action to take if vaccine storage units are not working properly is to protect the vaccine supply. If the problem is short term (usually 2 hours or less) and depending on ambient room temperature, the temperatures in the storage units can probably be maintained with water containers in the refrigerator, with frozen coolant packs in the freezer, and by keeping the unit doors closed. If there is an extended period of time before the situation can be corrected and there are no other storage units available on site, the vaccines should be moved to the back-up storage facility using the guidelines in the Emergency Vaccine Retrieval and Storage Plan (see the Storage and Handling Plans section). After this is accomplished, attempt to find the cause of the problem and correct it (see the Storage Troubleshooting section). Do NOT allow vaccines to remain in nonfunctioning units for an extended period of time while you attempt to resolve a problem.

## Slide 22: Thermometers
Calibrated Thermometers
For measuring vaccine storage unit temperatures, CDC recommends using only calibrated thermometers with a Certificate of Traceability and Calibration Testing.
This certificate informs user of a thermometer’s level of
accuracy compared to a recognized standard.
Notes: Thermometers are a critical part of good storage and handling practice. A storage unit is only as effective as the temperature monitoring system inside. Accurate temperature history that reflects actual vaccine temperatures is imperative to effective vaccine management. Every freezer and refrigerator unit used to store vaccine should have a calibrated thermometer.
Thermometer calibration must be tested annually or according to the manufacturer’s recommendation by a laboratory with accreditation from an International Laboratory Accreditation Cooperation (ILAC) Mutual Recognition Arrangement (MRA) signatory body.
When choosing a thermometer, look for high accuracy, +/-1°F (+/-.5°C). This information should be contained in the Certificate of Traceability and Calibration Testing (also known as a Report of Calibration).
Example of Thermometer Certificate of Traceability and Calibration Testing
All thermometers experience “drift” over time that affects their accuracy. When the Certificate of Traceability and Calibration Testing (also known as a Report of Calibration) expires, CDC recommends one of the following:
Have the accuracy of your thermometer tested by an accredited laboratory
Purchase a new thermometer with a Certificate of Traceability and Calibration Testing (also known as a Report of Calibration)
Contact your immunization program for resources on checking the accuracy of your thermometer

## Slide 23: Thermometer Characteristics
Continuous monitoring with active display
Alarm for out-of-range temperatures
Reset button if using data logger with min/max display
Shows current temperature as well as min/max temperatures
Be within +/- .5° C accuracy (+/- 1° F)
Low Battery Indicator
Notes: To ensure that refrigerators and freezers are maintaining the appropriate temperatures for vaccine storage, each unit should have a calibrated thermometer. Temperatures for each unit should be read and documented a minimum of twice each workday, including recording the minimum and maximum temperatures once each day. The temperature data, regardless of whether using paper or downloaded files, should be kept in a safe, retrievable place for at least 3 years. Several types of thermometers can be used to monitor the temperatures within vaccine storage units.
Based on studies of thermometers conducted by NIST in 2009, CDC recommends using a digital thermometer with a detachable probe that is immersed in a buffering material. A detachable probe facilitates downloading temperature data without removing the probe from the storage unit. NIST studies demonstrated that these probes in a thermal buffering material can more closely approximate the vaccine vial temperature when placed in the same area where the vaccine is stored.1

## Slide 24: Temperature Probes
Main digital display monitor outside storage unit
Probe immersed in a thermal buffer material inside unit attached to an external digital display monitor
Probe in a buffering material placed in proximity to vaccines
Notes: CDC recommends using temperature monitoring devices that allow for the main device to remain outside of the storage unit as this allows for reading temperatures without opening the unit door. The main device is attached to the internal temperature probe through a narrow cable (usually 1 to 3 meters long) with the probe placed in a thermal buffering material and positioned near the vaccine. To download data, the main unit can be easily disconnected from the cable, leaving the probe inside the storage unit.
CDC recommends having a back-up temperature probe for each vaccine storage unit, in the event that something happens to the primary temperature probe or if the primary probe needs to be sent to a laboratory for calibration. The back-up probe should have the same set up as the primary set up (i.e., temperature probe in a buffering material). In addition, CDC recommends that the back-up probe have a different calibration schedule than the primary probe so that your back-up is available when the primary probe is sent for calibration.

## Slide 25: Digital Data Loggers
Digital data loggers come in many shapes, sizes and styles and are typically battery operated.
Notes: CDC recommends the use of a continuous monitoring and recording digital data logger (DDL) with a current and valid Certificate of Calibration Testing (also known as a Report of Calibration), set at a minimum recording
interval of at least every 30 minutes.
Your facility should have a DDL for:
• Each vaccine storage unit
• Each emergency transport unit (this is particularly important if there are more transport units
than storage units)
• At least one backup DDL in case a primary device malfunctions or is out for calibration
testing (make sure the backup device has a different calibration testing schedule than the
primary device so it is available when the primary device is being tested)

## Slide 26: Digital Data Loggers
Hi/Lo alarm for out-of-range temperatures
Current temp., as well as min/max temps
Reset button
Low battery indicator
Accuracy of +/-1° F (0.5° C)
Memory storage of at least 4000 readings
User programmable logging interval (reading rate)
Notes: CDC recommends DDLs with the following characteristics:
• Detachable probe in a thermal buffered material (e.g., glycol, glass beads, sand, Teflon®)†
• Alarm for out-of-range temperatures
• Low-battery indicator‡
• Current, minimum, and maximum temperature indicator§
• Recommended uncertainty of +/-0.5° C (+/-1° F)
• Logging interval (or reading rate) that can be programmed by the user
Digital data logger thermometers used for vaccine storage are accompanied by special software that is installed on a computer. This software allows the user to set the frequency of the temperature readings, download data from the device, and calculate temperature averages, minimums, and maximums. To review the temperature history, the user must download data from the digital data logger thermometer on a regular basis.
Digital data logger thermometers have a variety of features in addition to their basic recording function. All contain a probe that is used to detect temperature readings. As stated previously, CDC recommends the use of thermal buffering material-encased probes, rather than air probes, because they provide a more accurate reading of actual vaccine temperature.

## Slide 27: Thermometers “NOT” Recommended
Fluid filled biosafe liquid thermometers
Bi-metal stem thermometers
Food thermometers and household mercury thermometers
Chart recorders
Infrared thermometers
Thermometers not calibrated
Notes: These thermometers can have significant limitations in vaccine temperature monitoring. They can be difficult to read and only indicate the temperature at the precise time they are read. Therefore, temperature fluctuations outside the recommended range may not be detected.
Certain types of temperature monitoring devices have significant limitations and should not be used to measure temperatures in a vaccine storage unit. These devices can be difficult to read and, because they only show the temperature at the exact time they are read, may fail to detect temperatures outside the recommended range. CDC does NOT recommend these temperature monitoring devices
Thermometers “NOT” Recommended:
Fluid filled biosafe liquid thermometers
Bi-metal stem thermometers
Food thermometers and household mercury thermometers
Chart recorders
Infrared thermometers
Thermometers not calibrated
Devices sold in hardware and appliance stores are generally designed to monitor temperatures for household food storage. They are not calibrated and not accurate enough to ensure vaccines are stored within the correct temperature range. Using these devices can pose a significant risk of damaging expensive vaccines.

## Slide 28: Thermometer Placement
Placement within the unit is just as important as thermometer selection. The thermometer should be in proximity to the vaccines being stored.
Thermometers should NOT be:
Placed in the doors
Near or against the walls
Close to vents
On the floor of the unit
Notes: Place the buffered probe of the DDL in the center of the unit with the vaccines surrounding it. A device placed near the walls, floor, vent, ceiling, or door may indicate temperatures that are colder or warmer than the actual vaccine temperature. This may not be true for pharmaceutical units because air flow and temperature are better regulated. Refer to your owner’s manual for instructions on temperature monitoring device placement.
• Place the DDL’s active digital display outside the unit so temperatures can be read without opening the door and disturbing the probe. The DDL should be set to measure temperatures at least every 30 minutes.

## Slide 29: Adjusting Storage Temperatures
Only the primary or alternate vaccine coordinator should adjust the temperature of a vaccine storage unit. A warning sign should be posted on the storage unit that says, “Do not adjust refrigerator (or freezer) temperature controls
Notes: Limiting access to the thermostat reduces the risk that the temperatures will be adjusted inappropriately. In some situations, the thermostat may need to be reset in summer and winter, depending on the ambient room temperature. If the thermostat requires adjustment, alert the vaccine coordinator or immediate supervisor.
Use caution in adjusting a thermostat. Normal defrost cycles and busy workdays can lead to slight temperature variations that are not necessarily indicative of inappropriate vaccine temperatures.
It may take 2 to 7 days to stabilize the temperature between 35°F and 46°F (2°C and 8°C) in a newly installed or repaired refrigerator. Likewise, it may take 2 to 3 days to stabilize the temperature between -58°F and +5°F (-50°C and -15°C) in a newly installed or repaired freezer. Allow one week of twice daily refrigerator and freezer temperature recordings, including minimum/maximum temperatures daily (preferably in the morning) to make sure temperatures are within the appropriate ranges before using the units to store vaccines.

## Slide 30: Temperature Variations
Temperatures can vary in a vaccine storage unit based on the contents, how often the door is opened, and power interruptions.
The only way to be sure the temperature in a storage unit has remained within the appropriate range is to frequently read and document the temperature using a calibrated thermometer.
Notes: Stabilizing the Temperatures with Water Bottles and Frozen Coolant Packs
You can help stabilize the temperature in the refrigerator by keeping at least two or three large containers of water inside. Store water bottles labeled “Do NOT drink” against the inside walls and in the door racks. You can help stabilize the temperature in the freezer by keeping frozen coolant packs inside.
Opening the Door
Limit the number of times the vaccine storage unit door is opened and avoid letting the door stand open unnecessarily. Not only does this affect the temperature in the unit, it also exposes the vaccines to light, which can reduce the potency of some vaccines (see CDC’s Vaccine Storage and Handling Guide for vaccine-specific recommendations). Routinely check the refrigerator and freezer doors throughout the day and at the end of each workday to ensure they are tightly closed.
Deli, Fruit, and Vegetable Drawers
Remove any deli, fruit, and vegetable drawers from the refrigerator. Removing the drawers not only provides extra space for storing containers of water, but it also removes the temptation to use the drawers for storage of food, beverages, or vaccines.

## Slide 31: Reading and Documenting Temperatures
Best Practices:
Post temperature log on storage unit
Read thermometer in both storage units twice daily (morning/end of work day)
Read min/max temperatures in both units a minimum of once each work day
Document readings for both units on temperature log
Record times of reading and staff initial who took reading
Download and review stored continuous monitoring data at least weekly
Notes: CDC recommends the routine vaccine storage and handling plan include reading and documenting storage unit temperatures a minimum of twice each workday, as well as the minimum/maximum temperatures daily (preferably in the morning). This best practice recommendation can prevent inadvertent loss of vaccine and the potential need for revaccination by assuring that temperature excursions are identified quickly so that immediate corrective action can be taken. This also provides an opportunity to visually inspect the storage unit, reorganize any vaccines that are inadvertently misplaced, and remove any expired vaccines.
CDC recommends the use of a continuous monitoring device/digital data logger to record and store temperature information at frequent programmable intervals for 24-hour temperature monitoring.
Stored temperature monitoring data should be downloaded and reviewed at least weekly by providers, both to ensure the timely review of the data and the appropriate response to issues. When the data is downloaded, the data logger should be reset so there is sufficient memory available. The downloaded information should be kept for a minimum of 3 years or according to individual state record retention requirements.

## Slide 32: Temperature Log
JM
73
8:00
Notes: CDC recommends on a twice daily basis:
• Check and record storage unit temperature readings each workday—in the morning
when you arrive and in the evening before leaving. This should be done even if there is a
temperature alarm or a DDL temperature monitoring device. A temperature monitoring log
sheet† should be placed on each storage unit door (or nearby), and the following information
should be recorded:
––Temperature
––Date
––Time
––Initials of person recording the data
If a reading is missed, leave a blank entry in the log.
CDC recommends on a weekly basis:
• Review storage unit temperature readings and review continuous DDL software or website
information for changes in temperature trends that might require action (adjusting unit
temperature or repairing/replacing storage or temperature monitoring equipment).
• File this information so it can be analyzed for long-term trends and/or recurring problems.
Temperature data should be kept for 3 years (unless state statutes or rules require a longer
period).
If other staff are monitoring and documenting the temperatures, the primary vaccine coordinator should review the temperature recording data weekly to ensure appropriate temperature documentation. If the vaccine coordinator is the person monitoring and documenting the temperatures, the alternate vaccine coordinator should review the data weekly.

## Slide 33: Avoiding Storage and Handling Mishaps

## Slide 34: Check Vaccine Shipments
Examine shipments on arrival
Examine container and contents for damage
Cross-check contents with the packing slip
Check the shipment date
Record shipment on an inventory log
Notes: #2: Check Vaccine Shipments
Your responsibility for proper vaccine storage and handling begins the moment the vaccine arrives. Vaccine shipments should be examined on arrival.
Examine the shipping container and its contents for any evidence of damage during transport.
Cross- check the contents with the packing slip to be sure they match.
Check the shipment date to determine how long the package was in transit to you. If the interval between shipment from the supplier and arrival of the product at its destination was excessive, particularly if the ice packs or dry ice has melted, it could mean the vaccine has been exposed to excessive heat or cold that might alter its integrity.
Finally, each shipment should be recorded on an inventory log. This log should include the name of each vaccine; the number of doses for each vaccine received; the date it was received; the condition of the vaccines upon arrival; the name of the vaccine manufacturers; the lot numbers; and the expiration dates for each vaccine.
If there are any discrepancies with the packing slip or concerns about the vaccine shipment, store the vaccine under proper conditions (do not automatically discard) and mark “Do Not Use” until the integrity of the vaccine is determined. You will then need to contact the state immunization office and manufacturer for further guidance.

## Slide 35: Location and Positioning
A best practice is to place vaccine in the central area of the storage space and keep vaccines in their original packaging inside storage trays positioned 2 to 3 inches away from storage unit walls.
Vaccine Spacing-allow for cold air circulation
Vaccine Packaging-similar packaging should be stored in different locations
Notes: Freezers
Vaccines should be stored away from the walls and vents in the part of the freezer best able to maintain the required temperature range (between -58°F and +5°F (-50°C and -15°C). Vaccines should not be stored in the freezer door. The temperature in the door is not stable and differs from that inside the unit. Frozen coolant packs can be stored in the freezer door.
Refrigerators
In the refrigerator, vaccines should be placed away from the walls, floor, and vents in the part of the unit best able to maintain the required temperature between 35°F and 46°F (2°C and 8°C). Vaccines should not be stored in the deli, fruit, and vegetable drawers, in the door, or on the floor of the unit.

## Slide 36: Labeling
Refrigerator Unit
Freezer Unit
Attach labels directly to the shelves on which the vaccines are placed, or label trays or containers according to the vaccines they contain
Notes: Labeling
The location of each specific vaccine type inside the storage unit should be clearly labeled. This can be accomplished by attaching labels directly to the shelves on which the vaccines are placed or by labeling containers in which packages of the same vaccine type are placed. Storing each vaccine type in its own specifically-labeled section of the refrigerator or freezer helps decrease the chance that someone will inadvertently administer the wrong vaccine. Label pediatric and adult versions of the same vaccine clearly to avoid confusion (see CDC’s Vaccine Labels for Storage Unit).
In addition to labeling the location of vaccines, mark each opened multidose vial with the date it was first opened. Mark reconstituted vaccine with the date and time it was reconstituted. Dating these vials is important for two reasons. First, some vaccines expire within a certain time after opening or after reconstitution (beyond use date [BUD]). The BUD varies among vaccines (see CDC’s Vaccine Storage and Handling Guide for specific vaccine product information). This may not correspond to the expiration date printed on the vial by the manufacturer. For example, multidose vials of MPSV4 should be discarded if not used within 35 days after reconstitution, even if the expiration date printed on the vial by the manufacturer has not passed. Second, dating opened or reconstituted vials helps manage vaccine inventory by identifying vials that should be used first.

## Slide 37: Trays and Containers
Trays and uncovered containers may be used to organize vaccine and diluent packages
This practice helps avoid medication errors
Trays and containers must not be stacked or placed closely that air circulation is impeded
Notes: Storage Containers
Vaccine and Diluent Packages
To avoid confusion, vaccine and diluent packages should be stored together by type and arranged in rows. Vaccines and diluents should be stacked according to expiration dates. Vaccines and diluents with the shortest expiration dates should be closer to the front of the storage unit for easy access. Store all opened and unopened vaccines and diluents in their original packaging inside the appropriate storage unit so that the contents and expiration dates are easily identifiable. Storing loose vaccine and diluent vials outside of their packaging is not recommended. This practice makes managing inventory and tracking expiration dates more difficult, increases administration errors when staff is confused about vials, and exposes the vaccines to light. Some diluents can be stored at room temperature (if they do not contain any antigen), separate from their corresponding vaccines. In this case, always assure that the correct diluent is used with the correct vaccine.
Trays and Containers
Trays and uncovered containers may be used to organize vaccine and diluent packages. Each tray or uncovered container should only contain vaccine or diluent of the same type. If other medications and biologic products must be stored in the vaccine storage unit, they must not be stored on the trays or in the containers with vaccine or diluent. This practice helps avoid medication errors. Clearly label the tray or container with the name of the vaccine or diluent, and place packages of that type on the tray or in the container inside the appropriate storage unit. Trays and containers must not be stacked or placed so closely together that air circulation inside the storage unit is impeded.

## Slide 38: Stock Rotation
New Shipments should be unpacked immediately
Check expiration date/rearrange the placement of vaccine and diluent in storage unit. Short-dated placed in front
Expired vaccines and diluents should NEVER be administered
Remove expired vaccines/diluents from unit
Notes: Keep Vaccines Organized
Check and rotate vaccine stock weekly so that vaccines with the shortest expiration dates are in the front to be used first.
If the expiration date on the vial is identified only as month and year, the vaccine does not expire until the LAST day of the month indicated on the vial.
  Expired vaccine - even if only one day after the expiration date- should NEVER be administered. Promptly remove expired vaccine from the refrigerator or freezer and dispose of it appropriately. If the expired vaccine is VFC vaccine, you should contact the GA VFC program so that the expired vaccine can be accounted for. Also as you check your vaccine expiration dates, when you note that you have vaccine that will expire before you can use all of it ( 3 months), you need to call the GA VFC program and let us know so we can have time to move it elsewhere.
  In addition, the same person should be responsible for documenting all vaccine wastage and making sure spoiled or expired vaccine is returned to the state.
Keep opened vials of vaccine in a tray, so that they are readily identifiable. Indicate on the label of each vaccine vial the date and time it was reconstituted or first opened. Influenza, pneumococcal polysaccharide, IPV, Td and tetanus toxoid are manufactured in multi-dose and single dose vials or syringes.
If your clinic situation permits, open only one vial, or box, of a particular vaccine at a time to control vaccine usage and allow easier inventory control. We also recommend that all opened vaccine vials be kept in a tray in the refrigerator separate from other medications and biologics to avoid medication errors.
To keep an accurate account of your inventory, keep your VFC vaccine stock separated from your privately purchased vaccine supply
Vaccine Stock Rotation
When new shipments arrive, vaccines should be unpacked immediately. The local practice vaccine coordinator should ensure that someone checks and rearranges the placement of vaccine and diluent supplies in the storage unit according to the expiration dates on a weekly basis and each time a vaccine shipment arrives. The vials and packages with the earliest expiration dates should be placed in front of other vials and packages of the same type of vaccine with later expiration dates. This practice avoids waste by ensuring that vaccines and diluents with the shortest expiration dates are easily accessible and will be used first, thereby limiting the amount of unused vaccine that has passed the expiration date. Expired vaccines and diluents should NEVER be administered. IMMEDIATELY remove expired vaccines and diluents from the storage unit(s) to avoid the risk of inadvertent use.

## Slide 39: Ensuring VFC Vaccine is administered only to Federally-Eligible Children
The Georgia VFC Program has always discouraged borrowing of VFC vaccine. New program changes require corrective action for providers found borrowing VFC vaccine for non-eligible patients.
NO BORROWING

## Slide 40: Vaccine Security
Protecting the Power Supply
Avoid using power outlets with built-in circuit switches
Use a safety-lock plug or an outlet cover
Post a warning sign at the plug and on the refrigerator and freezer units
Label the fuses and circuit breakers to alert people not to turn off the power to the storage units
Consider installing a temperature alarm to alert staff to after-hours temperature excursions
Back-up generators
Notes: To keep a storage unit temperature within the appropriate range, the unit must be in good working condition, and it must have power at all times. To prevent problems with the power supply, take the following steps:
Avoid using power outlets with built-in circuit switches (they have little red reset buttons), outlets that can be activated by a wall switch, or power strips. These can be tripped or switched off, resulting in loss of electricity to the storage unit.
Use a safety-lock plug or an outlet cover to reduce the chance of a unit becoming inadvertently unplugged.
Post a warning sign at the plug and on the refrigerator and freezer units alerting staff, janitors, electricians, or any workers not to unplug the units.
Label the fuses and circuit breakers to alert people not to turn off the power to the storage units. These labels should include information concerning the immediate steps to take if power is interrupted. When the practice is located in a building owned by a third party and providers do not have access to the circuit breaker, ask the building manager to assist in labeling the appropriate circuit. Consider installing a temperature alarm to alert staff to after-hours temperature excursions, particularly if large vaccine inventories are maintained.
Facilities storing large vaccine inventories should consider installing back-up generators that automatically provide power to the storage units to maintain the recommended storage temperatures in the event of power outages.

## Slide 41: Protecting Power Supply
Continuous-monitoring temperature alarm/notification systems
Avoid using power outlets with built-in circuit switches and outlets that can be activated by a wall switch.
Safety-lock plug
Consider using outlet covers. Post warning signs and labels.
Back-up generators

## Slide 42: Transporting Vaccine
Vaccine manufacturers do not generally recommend or provide guidance for transport of vaccines. If vaccines must be transported during an emergency or to an off-site facility, it is critical that vaccine potency is protected by maintaining the vaccine cold chain at all times.
Notes: Transport involves the movement of vaccine over a short time frame and distance between providers. The
time needed to transport should be fewer than 8 hours and vaccine should be placed in a stable
storage unit as quickly as possible. CDC does not recommend any shipment of vaccines from
your vaccine supply or any routine transport of vaccines.
Vaccines should only be transported when absolutely necessary (e.g., for a mass
immunization clinic, in an emergency, or to ensure vaccines that are about to expire† can be
used rather than wasted). Frozen varicella-containing vaccines should never be transported
except in an emergency.
If vaccines must be transported to an off-site facility, the amount of vaccines transported should be limited to the amount needed for that workday to avoid potential loss of expensive vaccines. Providers should contact manufacturer(s) and/or the state/local health department immunization program for guidance specific to their area.

## Slide 43: Transporting Vaccine
The facility Standard Operating Procedures (SOP) should specify that vaccines are:
Attended at all times during transport
Not placed in the trunk of the vehicle
Delivered directly to the facility
Promptly unpacked and placed into appropriate storage units upon arrival
Notes: Vaccines that will be used at an off-site or satellite facility should be delivered directly to that facility. If that is not possible, transport of vaccines should be done using a portable vaccine refrigerator with a temperature monitoring device placed with the vaccines. If this is not available, qualified containers and pack-outs can be used with a temperature monitoring device. If you must transport vaccines, transport only what is needed for the workday. The total time for transport and workday should be a maximum of 8 hours. If you must transport vaccines in non-commercial vehicles, use the passenger compartment—not the trunk.
Immediately upon arrival at an off-site/satellite facility, vaccines should be stored in an appropriate storage unit with a temperature monitoring device, and temperatures should be read and recorded a minimum of 2 times during the workday. If vaccines cannot be stored in an on-site storage unit, they should be kept in the portable
vaccine refrigerator during an off-site clinic:
• Place a temperature monitoring device (preferably with a probe in a thermal buffer) as
close as possible to the vaccines, and read and record temperatures at least hourly.
• Keep the container closed as much as possible.
• Remove only 1 multi-dose vial or 10 doses at a time for preparation and administration by
each person administering vaccines.

## Slide 44: Transporting Multidose Vials
When a multi-dose vial is used, FDA regulations require that it only be used in the facility where it was first opened.
Only if absolutely necessary, a partially used vial may be transported to or from an off-site facility operated by the same provider, as long as the vaccine cold chain is properly maintained
Notes: Varicella-containing vaccines may be transported at refrigerator temperature between 36°F and 46°F (2°C and 8°C) for up to 72 continuous hours prior to reconstitution (see Varicella-Containing Vaccines in CDC’s Vaccine Storage and Handling Guide). If varicella-containing vaccines must be transported at refrigerator temperature, follow these steps:
1. Place a calibrated thermometer (preferably with a biosafe glycol-encased thermometer probe) in the container used for transport as close as possible to the vaccines.
2. Record:
a. The time the vaccines are removed from the storage unit and placed in the container;
b. The temperature during transport;
c. The time and temperature at the beginning and end of transport.
3. According to the vaccine manufacturer, immediately upon arrival at the alternate storage facility:
a. Place the vaccines in the freezer between -58°F and +5°F (-50°C and -15°C) and label “DO NOT USE.” Any stand-alone freezer that reliably maintains a temperature between -58°F and +5°F (-50°C and -15°C) is acceptable for storage of varicella-containing vaccines.
b. Document the time the vaccines are removed from the container and placed in the alternate storage unit.
c. Note that this is considered a temperature excursion, so contact the manufacturer at 1-800-637-2590 for further guidance.
4. Do not discard vaccines without contacting the manufacturer and/or your immunization program for guidance.
Use of dry ice is not recommended, even for temporary storage or emergency transport. Dry ice may subject varicella-containing vaccines to temperatures colder than -58°F (-50°C).

## Slide 45: Transporting Varicella-Containing Vaccines
The vaccine manufacturer does not recommend transporting varicella-containing vaccines (MMRV, VAR, HZV). If these vaccines must be transported (e.g., during an emergency), CDC recommends transport in a portable freezer unit that maintains the temperature between -58°F and +5°F (-50°C and -15°C).
Do Not Use Dry Ice
Notes: If necessary, varicella-containing vaccines that have not been reconstituted may be
transported at refrigerated temperatures. However, you must contact the vaccine
manufacturer for guidance upon arrival at off-site/satellite facility.

## Slide 46: Transporting Varicella-Containing Vaccines
Varicella-containing vaccines may be transported at refrigerator temperature between 36°F and 46°F (2°C and 8°C) for up to 72 continuous hours prior to reconstitution. If varicella-containing vaccines must be transported at refrigerator temperature, follow these steps:
Place calibrated thermometer in container
Record time vaccines and placed in container, temperature during transport, and time and temperature at the beginning and end of transport
Immediately, upon arrival at alternate storage facility, place vaccines in the freezer between -58°F and +5°F (-50°C and -15°C) and label “DO NOT USE.” Document time the vaccines are removed from the container and placed in alternate storage unit. Note that this is considered a temperature excursion, so contact the manufacturer for further guidance
Do not discard vaccines without contacting the manufacturer and/or your immunization program for guidance
Notes: Transporting Varicella-Containing Vaccines
The vaccine manufacturer does not recommend transporting varicella-containing vaccines (MMRV, VAR, HZV). If these vaccines must be transported (e.g., during an emergency), CDC recommends transport in a portable freezer unit that maintains the temperature between -58°F and +5°F (-50°C and -15°C). Portable freezers may be available for rent in some places. If varicella-containing vaccines must be transported and a portable freezer unit is not available, do NOT use dry ice.
Varicella-containing vaccines may be transported at refrigerator temperature between 36°F and 46°F (2°C and 8°C) for up to 72 continuous hours prior to reconstitution (see Varicella-Containing Vaccines in CDC’s Vaccine Storage and Handling Guide). If varicella-containing vaccines must be transported at refrigerator temperature, follow these steps:
1. Place a calibrated thermometer (preferably with a biosafe glycol-encased thermometer probe) in the container used for transport as close as possible to the vaccines.
2. Record:
a. The time the vaccines are removed from the storage unit and placed in the container;
b. The temperature during transport;
c. The time and temperature at the beginning and end of transport.
3. According to the vaccine manufacturer, immediately upon arrival at the alternate storage facility:
a. Place the vaccines in the freezer between -58°F and +5°F (-50°C and -15°C) and label “DO NOT USE.” Any stand-alone freezer that reliably maintains a temperature between -58°F and +5°F (-50°C and -15°C) is acceptable for storage of varicella-containing vaccines.
b. Document the time the vaccines are removed from the container and placed in the alternate storage unit.
c. Note that this is considered a temperature excursion, so contact the manufacturer at 1-800-637-2590 for further guidance.
4. Do not discard vaccines without contacting the manufacturer and/or your immunization program for guidance.
Use of dry ice is not recommended, even for temporary storage or emergency transport. Dry ice may subject varicella-containing vaccines to temperatures colder than -58°F (-50°C).

## Slide 47: Vaccines and Diluents for Transport
CDC recommends transport with a portable refrigerator unit. If this type of unit is not available, a hard-sided insulated cooler with at least 2-inch walls may be used if it can maintain the recommended temperature range (between 36°F and 46°F [2°C and 8°C]).
Refrigerated/frozen coolant packs
Place bubble wrap or Styrofoam pellets between the refrigerated or frozen coolant packs and the vaccines.
Notes: Packing Vaccines and Diluents for Transport
There are many variables to consider when transporting any vaccine (e.g., the time of year and ambient temperature, the amount of vaccine, the shipping container, etc.) Your immunization program may have specific guidance regarding vaccine transport, details on how to pack vaccine and diluent, and procedures for maintaining the vaccine cold chain based on these variables. Here is some general guidance.
Refrigerated vaccines
● Pack refrigerated vaccines before packing frozen vaccines as indicated here: CDC recommends transport with a portable refrigerator unit. If this type of unit is not available, a hard-sided insulated cooler with at least 2-inch walls may be used if it can maintain the recommended temperature range (between 35°F and 46°F [2°C and 8°C]).
● Place a layer (at least 2 inches) of “conditioned” coolant packs in the transport container first. Coolant packs that are frozen must be “conditioned” by leaving them at room temperature for 1 to 2 hours until the edges have defrosted and the packs look like they’ve been “sweating.” Frozen coolant packs that are not “conditioned” can freeze vaccine.
Place an insulating barrier layer on top of the coolant packs, (e.g., bubble wrap or Styrofoam pellets).
Place a calibrated thermometer (preferably with a biosafe glycol-encased thermometer probe) on top of the barrier next to the vaccines.
Stack the vaccines on top of the barrier and thermometer, ensuring that the vaccines do not touch the coolant packs.
Place another insulating barrier layer on top of the vaccines.
Place another layer of “conditioned” coolant packs on top of the insulating barrier layer, ensuring there is no direct contact between the coolant packs and the vaccines.
Place a final insulating barrier layer (at least 2 inches) on top of the coolant packs along with an inventory list of the vaccines in the container
Frozen vaccines
If frozen vaccines must be transported, CDC recommends transport with a portable freezer that maintains a temperature between -58°F and +5°F (-50°C and -15°C). Use the same packing layers as noted above.
The coolant packs should be frozen. Do NOT use dry ice.
Diluents
● Diluents should be transported with their corresponding vaccines to ensure that there are always equal numbers of vaccine vials and diluent vials for reconstitution. NEVER transport any diluents at freezer temperature because the vials could crack, or in some cases, the diluents may contain vaccine antigen.

## Slide 48
ACTION PLANS

## Slide 49: Standard Operating Procedures (SOP)
It is important to establish routine, systematic procedures for handling vaccine shipments. Each facility should develop its own written standard operating procedures to address:
Receiving Vaccine Shipments
Checking the Condition of a Shipment
Storing and Documenting Vaccine Shipments Upon Arrival
Notes: Receiving Vaccine Shipments
Arrange for vaccine deliveries to be made only when the vaccine coordinator or alternate coordinator is on duty. Consider holidays, vacations, staff schedules, and changes in hours of operation when designating vaccine delivery date and time. All staff members (including non-medical staff, e.g., receptionists and other front desk personnel) who accept vaccine deliveries must be aware of the importance of maintaining the vaccine cold chain and the need to immediately notify the vaccine coordinator or alternate coordinator of the arrival of the vaccine shipment so that it can be handled and stored appropriately.
Checking the Condition of a Shipment
When you receive your vaccine shipment, it should be examined immediately:
Examine the shipping container and its contents for any signs of physical damage. Determine if the shipping time was less than 48 hours (3 days for varicella-containing vaccines). Cross-check the contents with the packing slip to be sure they match. Check the vaccine expiration dates to ensure that you have not received any vaccines or diluents that have already expired or will expire soon. Check that lyophilized (freeze-dried) vaccines have been shipped with the correct type and quantity of diluents for reconstitution. Examine the vaccines and diluents for heat or cold damage.
Storing and Documenting Vaccine Shipments Upon Arrival
After the vaccine shipment has been checked according to the procedures described in this section (see Checking the Condition of a Shipment), immediately store the vaccines and diluents at the recommended temperatures and record the arrival of each vaccine and diluent, noting all the details as outlined in the Vaccine Stock Records (see the Vaccine Inventory Management section).

## Slide 50: Routine Storage and Handling Plan
Each Routine Vaccine Storage and Handling Plan should include:
Up-to-date contact information for:
-Primary and alternate vaccine coordinators
-Immunization program (VFC Contact)
-Manufacturers of the vaccines
-Refrigerator/freezer maintenance and
repair companies
-Utility/power company
-Vaccine storage unit alarm company
-Sources of packing materials and calibrated
thermometers

## Slide 51: Routine Storage and Handling Plan
Descriptions of the roles/responsibilities or primary and alternate coordinators
Policy on education and training for staff
Protocols for ordering and accepting vaccine deliveries
Summaries of the storage requirements for each vaccine and diluent
Protocols for vaccine storage unit temperature monitoring
Protocols for vaccine storage equipment maintenance
Protocols for the correct placement of vaccines within storage units

## Slide 52: Routine Storage and Handling Plan
Protocols for responding to vaccine storage and handling problems
Protocols for vaccine inventory management
Protocols for transporting and receiving shipments
Protocols for handling vaccine prior to administration
Protocols for proper disposal of vaccines and supplies
Samples of the forms used in your vaccination program
Notes: Keep your Routine Vaccine Storage and Handling Plan in a prominent and easily accessible location near the vaccine storage unit(s). Also establish a checklist of procedures and post it on all vaccine storage unit(s) (see the IAC link to a Checklist for Safe Vaccine Handling and Storage in the Resources section).

## Slide 53: Storage Troubleshooting
Immediate Action must be taken to correct improper vaccine storage conditions, including inappropriate exposure to light and exposure to storage temperatures outside the recommended ranges.
Actions should be documented and include:
  Date and Time of occurrence
  Ambient room and storage unit temperatures
  Description of problem
  Action taken
  Outcome
  Initials of the person documenting the incident
Notes: If you become aware of inappropriate vaccine storage conditions (light and/or temperature), the following steps should be taken:
Notify the primary or alternate vaccine coordinator immediately of any vaccine storage unit temperature that is outside the recommended range (temperature excursion). If the primary coordinator or alternate coordinator is not available, report the problem to an immediate supervisor.
Document the ambient room temperature and the temperature inside the affected storage unit(s) at the time the problem is discovered. Also note minimum and maximum temperature readings in the unit(s). Document the length of time the vaccines may have been exposed to inappropriate storage temperatures or inappropriate light exposure. The temperature information should be available to download from a digital data logger. Conduct an inventory of the vaccines affected by this event and document the actions taken. Note if water bottles were in the refrigerator and frozen coolant packs in the freezer at the time of the event. Label the vaccines “DO NOT USE.” A clearly labeled paper bag can be used for this purpose. This will reduce risk of inadvertently using vaccines that may have reduced potency because they were stored under inappropriate conditions. Immediately store the vaccines under appropriate conditions separate from other vaccine supplies. If your vaccine storage unit(s) is not maintaining the appropriate storage conditions, activate the Emergency Vaccine Retrieval and Storage Plan (see Storage and Handling Plans). Contact the vaccine manufacturer for further guidance. If you are a VFC provider, please contact the vaccine manufacturer and/or your state/local health department immunization program as directed by the VFC program in your area. Do not discard vaccines unless directed to by your immunization program and/or the manufacturer(s).

## Slide 54: Emergency Vaccine Retrieval and Storage Plan
You should have the following in place:
Designated primary and alternate coordinator with emergency contact info
Emergency staff contact list in order of contact preference
Vaccine storage unit specifications
Alternate vaccine storage facility or facilities
Written protocols, vehicles and drivers for transporting vaccines to and from the alternate vaccine storage facility
Notes: General Guidelines
To protect the vaccine inventory and to minimize potential monetary loss, every facility that stores vaccine should have a written Emergency Vaccine Retrieval and Storage Plan. If a problem is short term (usually 2 hours or less) and depending on ambient room temperature, the storage temperature can probably be maintained with the water containers in the refrigerator, with frozen coolant packs in the freezer, and by keeping the storage unit door(s) closed.
Post the Emergency Vaccine Retrieval and Storage Plan on or near the vaccine storage equipment. Ensure that all staff (current, new, and temporary) read the plan and understand it. Also ensure that janitorial and security staff are aware of the plan and know the procedures to follow to notify designated personnel about any problems with the vaccine storage equipment or power outages. Review and update the contact lists in the plan at least quarterly; review and update the entire plan at least annually.
When state officials, local officials, or providers have reasonable cause to believe that weather conditions, natural disasters, or other emergencies might disrupt power in or flood any facility where vaccine is stored, emergency procedures should be implemented in advance of the event.

## Slide 55: Emergency Vaccine Retrieval and Storage Plan
Written instructions for entering your facility and vaccine storage spaces in an emergency if the building is closed
Appropriate packing materials to safely transport or temporarily store vaccine
Written protocol for vaccine packing
Notes: Designated primary and alternate vaccine coordinators with emergency contact information. In addition to their routine vaccine storage and handling duties (see the Vaccine Personnel section for details), the primary and alternate vaccine coordinators should:
Monitor the operation of the vaccine storage equipment and systems;
Track inclement weather conditions;
Set up and maintain a monitoring/notification system during times of inclement weather or other conditions that might cause a power outage (a continuous-monitoring temperature alarm/notification system should be considered, especially for facilities with large inventories);
Post emergency contact information on circuit breaker(s) or electrical panel; Ensure the appropriate handling of vaccine during a disaster or power outage; Ensure 24-hour access to the building and vaccine storage unit(s); Ensure that sufficient fuel is on hand to continuously run the generator for at least 72 hours if the facility has a back-up generator.
Emergency staff contact list in order of contact preference. Determine whether all or certain persons on the list should be contacted in the event of a vaccine storage emergency or if the first person reached is sufficient. Include the primary and alternate vaccine coordinators on the list. Record the names (in order) and contact information. Assure that contact information is kept up to date
Vaccine storage unit specifications. For each vaccine storage unit in your facility, identify the type of unit (e.g., stand-alone refrigerator), the brand name, the model number, and the serial number. These specifications may be useful for the repair company.
Alternate vaccine storage facility or facilities. Establish working agreements with at least one alternate storage facility with a back-up generator where vaccines can be appropriately stored and monitored for the interim (e.g., hospital, long-term care facility, state depot, Red Cross, fire station, packing plant, commercial pharmacy).
Written protocols, vehicles, and drivers for transporting vaccines to and from the alternate vaccine storage facility.
– If the vaccines must be moved to an alternate facility, they may be transported in portable actively or passively cooled refrigerator or freezer units or hard-sided insulated containers. The vaccines may be transported within non-commercial vehicles inside the passenger compartment (not in the trunk because temperatures cannot be controlled inside the trunk).
Appropriate packing materials to safely transport or temporarily store vaccine. Vaccine manufacturers do not recommend reuse of shipping materials, including coolant packs and shipping containers, to further transport vaccine products
Written protocol for vaccine packing. Each facility should develop its own standard operating procedures (SOPs) for packing vaccines

## Slide 56: Routine and Emergency Vaccine Handling Plan
Notes: This slide represent the document for Routine and Emergency Vaccine Handling Plan Templates which providers can use as a guideline to follow developing routine and emergency handling plans. They should be posted near your storage unit or where they can be easily accessed in case of an emergency.

## Slide 57: VACCINE ACCESS
Only authorized personnel should have access to the vaccine supply. This will help to protect the vaccine supply by avoiding inappropriate removal of vaccines or inappropriate handling of vaccines and vaccine storage units by untrained personnel.
Notes: Authorized personnel should be trained to interpret expiration dates, how to handle mishandled vaccines and diluents, transferring vaccines and diluents, rotating stock and documenting vaccine inventory.

## Slide 58: Trivia Challenge
Which staff need to be trained on vaccine storage and handling?
Only staff who administer vaccines
Only the primary and alternate vaccine coordinators
Only new staff during orientation
All staff who handle or administer vaccines, including accepting shipments
Notes: D) All staff who handle or administer vaccines, including accepting shipments

## Slide 59: Trivia Challenge
Which statement best defines cold chain
management?
Checking that vaccines are potent and effective when used
Maintaining proper storage temperatures at every link in the chain
Minimizing exposure to excessive heat or cold
Checking vaccines for physical evidence of lost potency before administration
Notes: B) Maintaining proper storage temperatures at every link in the chain

## Slide 60: Trivia Challenge
You are a staff member and notice that a
vaccine storage unit is not working
correctly. What needs to be taken
immediately?
Move the vaccines to the staff lounge refrigerator
Notify the vaccine coordinator, alternate coordinator, or supervisor
Throw out all the vaccines in the failed unit
Attempt to fix the unit
Notes: Notify the vaccine coordinator, alternate coordinator, or supervisor

## Slide 61: Take-Home Messages
  A proper cold chain is a temperature-controlled supply chain that includes all equipment and procedures used in the transport and storage and handling of vaccines from the time of manufacturer to administration of the vaccine.
  Out of range temperature readings require IMMEDIATE action
  For patients to be protected by the vaccines it is your responsibility to handle vaccines with care.
  Vaccine management, including proper storage and handling procedures, is the basis on which good immunization practices are built.
Notes: An estimated 17% to 37% of providers expose vaccines to improper storage temperatures, and refrigerator temperatures are more commonly kept too cold than too warm.
Colder is NOT BETTER for inactivated vaccines.
Out of range temperature readings require IMMEDIATE action.
Remember, if you want your patients to be protected by the vaccines you give them, it is your responsibility to handle vaccines with care.
Good practices to maintain proper vaccine storage and handling can ensure that the full benefit of immunizations are realized.

## Slide 62: Storage and Handling Resources
Providers should review helpful vaccine management material
available via the following links:
CDC’s Vaccine Storage and Handling Home Page http://www.cdc.gov/vaccines/recs/storage/default.htm
CDC’s Storage and Handling Toolkit http://www.cdc.gov/vaccines/recs/storage/toolkit/storage-handling-toolkit.pdf (Contact your Immunization Program Consultant for a hard copy)
You Call the Shots: Vaccine Storage and Handling Module – An interactive, web-based module that provides learning opportunities, self-test practice questions, reference and resource materials, and an extensive glossary. http://www.cdc.gov/vaccines/ed/youcalltheshots.htm
http://www.cdc.gov/vaccines/default.htm
http://www.immunize.org

## Slide 63: http://dph.georgia.gov/immunization-section
Notes: The Immunization Program webpage contains various helpful information. The webpage address is at the top of the slide.

## Slide 64: Resources
Local health department
District Immunization Coordinator
GA Immunization Program Office
  On call Help line: 404-657-3158
  GRITS Help Line: 1-866-483-2958
  VFC Help Line:1-800-848-3868
  Website: https://dph.georgia.gov/immunization-section
  Your local Immunization Regional Consultant (IRC)
GA Chapter of the AAP
GA Academy of Family Physicians
Notes: If you need further information about the changes, or to ask questions later, these are some resources you can to go to help you with that.
Local health department
District Immunization Coordinator
GA Immunization Program Office
  404-657-3158
  Website http://health.state.ga.us/programs/immunization
GA Chapter of the AAP
GAFP